## Slide 1
July 26th, 2016
EMSEC/SHA Blockseminar
Side-Channel Attacks on Implementations of Lattice-Based Cryptosystems
Felix Haarmann, Julian Speith

## Slide 2: WHAT?!?
Todays digital infrastructure is based on public-key crypto
Current public-key crypto vulnerable to quantum computing
  Shor’s algorithm for prime factorization and discrete logarithms
Quantum computers might become feasible in near future
Urgent need for post-quantum crypto
Lattice-based crypto is one possible solution
  Currently most promising one, as it is pretty efficient
Side-Channel attack resistance is important for future implementations

## Slide 3: Structure of our Presentation
Some Basics...
Ring-LWE Encryption Scheme
  Masking using a masked decoder
BLISS (Bimodal Lattice Signature Scheme)
  Sampling algorithms
  Cache attacks

## Slide 4: Some Basics... Ideal Lattices and Learning with Errors over Rings
Set of linear independent vectors
Generated by all linear combinations of those vectors
Ideal lattice corresponds to ideals in a ring
  Enables more efficient arithmetics over polynomial rings
Ring-LWE problem is a lattice-based problem
  considered hard to solve

## Slide 5: Some Basics... Side-Channel Attack Terminology (DPA)
Conclude secret information using leakages
One type of attack: Differential Power Analysis (DPA)
  Sensitive variable: Value that depends on the secret key and the plaintext
Countermeasure: Masking
  -th order masking: Split a sensitive variable into independent shares
Defeat masking: Higher-Order DPA (HO-DPA)
  Usage of leakages corresponding to shares of a sensitive variable
  -th order DPA defeats -th order masking
  HO-DPA difficult due to increasing noise effects

## Slide 6: Ring-LWE Encryption Scheme Overview
All polynomials are elements of the ring
Globally known: parameters , polynomial
  : Dimension of the ring (degree of )
  : Modulus of the coefficients of polynomials in
  : Standard deviation of a discrete Gaussian distribution
Three main operations:
  Key Generation (not shown)
  Encryption (shortened)
  Decryption (main focus)

## Slide 7: Ring-LWE Encryption Scheme Encryption
Input: -bit message , public key
Encode as an element of by multiplying each bit with
  Encoded message is denoted as
Do some math …
Output: Ciphertext

## Slide 8: Ring-LWE Encryption Scheme Decryption
Input: Ciphertext , secret key
Compute
Decode with a function
  is the -th coefficient of
Output: Message

## Slide 9: Masking Using a Masked Decoder Overview
Focus on decryption of ring-LWE scheme
All operations in NTT domain (Number Theoretic Transform)
Split the secret key into and such that

## Slide 10: Masking Using a Masked Decoder Masked Decoder I
Recall:
We can state eight rules based on the quadrants of and
  e.g.: and

## Slide 11: Masking Using a Masked Decoder Masked Decoder II
Recall:
If no rule is met (right two cases), refresh and repeat
  Refresh: and for
  Satisfactory results for iterations

## Slide 12: Masking Using a Masked Decoder Masked Table Lookup
Implement said rules in a masked table

## Slide 13: Masking Using a Masked Decoder Evaluation I
First-order DPA with masking turned off
(left) and (right) can be seen in red
Attack is successful

## Slide 14: Masking Using a Masked Decoder Evaluation II
First-order DPA with masking turned on
(left) and (right) can be seen in red
Attack is not successful

## Slide 15: Masking Using a Masked Decoder Evaluation III
1st-order DPA (left) and 2nd-order DPA (right), masking on
can be seen in red
Second-order DPA is successful, while first-order DPA is not
  Assures that the setting is correct

## Slide 16: BLISS Unterüberschrift
Bitte “Structure of presentation” in Folie 2 an deinen Aufbau anpassen, alles was da aufgelistet ist kommt irgendwo als Überschrift einer Folie vor

## Slide 17
Thank you for your attention! Any Questions?
July 26th, 2016
EMSEC/SHA Blockseminar
Side-Channel Attacks on Implementations of Lattice-Based Cryptosystems
Felix Haarmann, Julian Speith